## Slide 1: 數位IC設計 Tool安裝&作業模擬教學
NCKU CSIE DICLAB

## Slide 2: The simulation process
The simulation process and the necessary tools in this class
The tools can be downloaded from :
  https://www.intel.com/content/www/us/en/software/programmable/quartus-prime/download.html#
Functional simulation
Synthesis
Gate Level simulation
ModelSim
Quartus
ModelSim

## Slide 3: Download and install Quartus

## Slide 4: Download and install Quartus
Step 1: Register and sign in
Click here to create an account and sign in

## Slide 5: Download and install Quartus
Step 2: Click “ Download for Windows(free, no license required)“
Click Here

## Slide 6: Download and install Quartus
Step 3: Select software version (20.1.1)
Select version 20.1.1

## Slide 7: Download and install Quartus
Step 4: Download Quartus setup execution file
1. Click the ‘Individual Files’ tab
2. Download Quartus

## Slide 8: Download and install Quartus
Step 5: Installation

## Slide 9: Download and install Quartus
Step 5: Installation
2. Click
1. Accept the agreement
3. Set installation path
4. Click

## Slide 10: Download and install Quartus
Step 5: Installation
2. Click
1. Select Quartus Prime Lite Edition (Free)
4. Click
3. Check available disk space

## Slide 11: Download and install Quartus
Step 5: Installation
2.Click
1. Cancel check driver installation

## Slide 12: Download and install Quartus
Step 6: Download device support file
Download Cyclone IV Device Support

## Slide 13: Download and install Quartus
Step 7: Install Device
  Windows搜尋 > Device Installer
1. Select path of device support file
2. Click
3. Check Devices & Cyclone IV
4. Click

## Slide 14: Download and install Quartus
Step 7: Install Device
1. Check available disk space
2. Click
3. Click

## Slide 15: Synthesis by Quartus

## Slide 16: Synthesis by Quartus
Step1: Create a new project
  File -> new project wizard
Click here

## Slide 17: Synthesis by Quartus
Step1: Create a new project
Click here
The project name should be
as same as the name of top module
Modify the project path
Don’t use the default path

## Slide 18: Synthesis by Quartus
Step1: Create a new project
  Add the file excepting the testbench
2. Click here
3. Click here
1. Select Empty project
4. Select all .v files except the testbench
5. Click here

## Slide 19: Synthesis by Quartus
Step2: Select the device : EP4CE55F23A7
1. Select device family (Cyclone IV E)
2. Select device
3. Click here

## Slide 20: Synthesis by Quartus
Step 3 : Gate level simulation configuration
  select ModelSim-Altera and Verilog HDL
Click
Click

## Slide 21: Synthesis by Quartus
Step 4 : compile
  Assignment > Settings > Simulation > More EDA Writer Settings
Off

## Slide 22: Synthesis by Quartus
Step 4 : compile
Click

## Slide 23: Gate-Level Simulation by ModelSim

## Slide 24: Gate-Level Simulation by ModelSim
Step 1 : the gate level file (*.vo,*.sdo) can be found in simulation/modelsim folder, and put them into modelsim project directory created in functional simulation section.
  Simulation folder is in the Quartus project directory created in the synthesis section.

## Slide 25: Gate-Level Simulation by ModelSim
Step 2 : gate level simulation
  (Simulate -> Start Simulation Window)
  This time, use the *.vo for simulation ( Replace the original top_module.v with *.vo )
  Repeat the steps of functional simulation. ( Need to cancel the no timingchecks. )

## Slide 26: Gate-Level Simulation by ModelSim
Step 2: Gate Level Simulation
  Add cycloneive and altera library to search libraries ( click Libraries to add )
    your quartus installation disk/altera/13.0sp1/modelsim_ase/altera/Verilog/cycloneii
  Add *.sdo to SDF Files and fill the instance name of your design in testbench.v in “apply to region” (click SDF to add)
Testbench file